Name	Description	Units	Address
Version Number	1.1.0
Build Date	11/4/2016
Last Editor	Evin Ballantyne
Controller output current rating	The drive maximum phase current rating	Amps	0
Controller input voltage rating	The drive maximum input voltage rating	Volts	1
Switching frequency	The switching frequency of the 3 phase bridge	Hertz	2
Dead time	The time interval during which MOSFETS of the same bridge leg can't be turned on concurrently	ns	3
Baud rate	Communications represents the number of symbols transferred per second	Baud	4
Slave ID	Multi drop slave ID	Node #	5
HW configuration vector	15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0 1=enabled 0=disabled bit 0: Active low hardware overcurrent bit 1: Reserved bit 2: Power supply control of current sensor bit 3: enable DPWM mode bit 4: HW slave ID bit 5: HW parameter select bit 6: Light sensor bit 7: Reserved bit 8: Locked parameters bit 9: Inverted cutoff brake 1 bit 10: Enable 6 Step mode bit 11: Reserved bit 12: Reserved bit 13: Reserved bit 14: Current scaling x8 bit 15: Reserved		6
Current regulator Kp	The current regulator's proportional gain		7
Current regulator Ki	The current regulator's integral gain		8
Speed regulator Kp	The speed regulator's proportional gain		9
Speed regulator Ki	The speed regulator's integral gain		10
Speed regulator mode	0 is speed / 1 is torque / 2 is torque mode with speed limiting		11
Pll Kp old	The old phase locked loop's proportional gain		12
Pll Ki old	The old phase locked loop's integral gain		13
Phase A current gain	Current feedback gain at the ADC	Amps/Volt	14
Voltage gain	Voltage feedback gain (Vdc and Vphase) at the ADC	Volts/Volt	15
Phase C current gain	Current feedback gain at the ADC	Amps/Volt	16
Throttle gain	Throttle feedback gain at the ADC	Volts/Volt	17
Brake gain	Brake feedback gain at the ADC	Volts/Volt	18
BMS gain	BMS feedback gain at the ADC	Volts/Volt	19
DC voltage filter shift	DC voltage measurement low pass filter shift value in bits	bits	20
Temperature filter shift	Temperature measurement low pass filter shift value in bits	bits	21
DQ axis filter shift	DQ axis low pass filter shift value in bits	bits	22
Flux filter shift	Flux filter shift value in bits	bits	23
Flux hpf shift	Flux high pass filter shift value in bits	bits	24
Flux frequency filter shift	Flux frequency filter shift value in bits	bits	25
Voltage feedback filter cutoff frequency	Voltage feedback filter cutoff frequency	Hertz	26
Averaged over current trip threshold	Averaged phase current over current threshold	Amps	27
Averaged over current trip sample length	Number of phase current samples the averaged current is based on	samples	28
Instantaneous over current trip threshold	Instantaneous over current trip threshold	Amps	29
Phase Current RMS Filter Shift	Phase Current RMS Filter Shift	counts	30
Maximum interrupt execution time	Maximum allowable ISR execution time as fraction of the base ISR time	pu	31
Command timeout threshold	Maximum allowable amount of time between valid command packets for comm dropour detection	ms	32
DC voltage trip clear hysterisis	% of rated system voltage below trip threshold required to clear the over voltage fault	% of rated system voltage	33
Heatsink over temperature trip threshold	Maximum controller temperature	deg C	34
Controller foldback starting temperature	Controller temperature at which output current foldback begins	deg C	35
Controller foldback ending temperature	Controller temperature at which output current is folded back to 0 Amperes	deg C	36
Controller temperature feedback V at 0 C	Controller temperature sensor's output voltage at 0 C	Volts	37
Controller temperature feedback V at 25 C	Controller temperature sensor's output voltage at 25 C	Volts	38
Controller temperature feedback V at 50 C	Controller temperature sensor's output voltage at 50 C	Volts	39
Controller temperature feedback V at 75 C	Controller temperature sensor's output voltage at 75 C	Volts	40
Controller temperature feedback V at 100 C	Controller temperature sensor's output voltage at 100 C	Volts	41
Controller temperature feedback V at 125 C	Controller temperature sensor's output voltage at 125 C	Volts	42
Reserved L3 21			43
Reserved L3 22			44
Antitheft enable time	Time since bootup to allow enabling of the anti theft feature (0 to always allow)	ms	45
Kd anti theft	Speed proportional term for anti theft feature defined in per unit current / per unit speed	pu/pu	46
Open circuit voltage test window	Open circuit test voltage bounds	V (norm)	47
High/Lowside turn on voltage test window	Hi/Lo side turn on test voltage bounds	V (norm)	48
Average Command timeout threshold	Maximum allowable average amount of time between valid command packets (for slow update rate or missed packets)	ms	49
Remote comm loss braking current limit	Per unit braking current limit for communication loss, where the speed setpoint is set to zero	pu	50
Current Regulator bandwidth	When non-zero is used with Rs and Ls to calculate the Kp and Ki terms	radians	51
PLL bandwidth	When non zero sets the PLL Kp and Ki terms	radians	52
PLL damping	When non zero sets the PLL Kp and Ki terms		53
Pll Kp	new PLL Kp gain		54
Pll Ki	new PLL Ki gain		55
CAN baud rate	CAN baud rate in kbps (legal values 1000,500,250 or 125 )	kbps	56
CAN ID	CAN ID		57
communications configuration vector	15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0 1=enabled 0=disabled bit 0: Extended 29 bit ID bit 1: CAN faults bit 2: Enable LIN bit 3: Enable sleep on sync loss bit 4: Enable auto operational bit 5: Reserved bit 6: Reserved bit 7: Reserved bit 8: Reserved bit 9: Reserved bit 10: Reserved bit 11: Reserved bit 12: Reserved bit 13: Reserved bit 14: Reserved bit 15: Reserved		58
Battery resistance	Reserved for future use	milliohms	59
New Phase A current gain	Current feedback gain at the ADC, when zero, auto migrated in rev 5.8.11 from old gains and hwconfig bit 14	Amps/Volt	60
New Phase C current gain	Current feedback gain at the ADC, when zero, auto migrated in rev 5.8.11 from old gains and hwconfig bit 14	Amps/Volt	61
Flash parameter read access code	When not zero, you will need to enter this code to read parameters (only checked at bootup)		62
Hall stall fault time	Time to fault when no change of state on hall signals and running with >20% motor current	msec	63
Baud rate port2	Communications represents the number of symbols transferred per second	Baud	64
Slave ID port2	Multi drop slave ID for second comm port	Node #	65
Display protocol	0=disabled, 1=SWLCD open 9 mode, 2=SWLCD(closed) ,3=reserved, 4= KM5 (open) 9mode, 5= KM5 (open) 5mode, 6=Wuxing 3 mode		66
Saved software revision	Software version when parameters were last saved to flash memory		67
Kp anti theft	Position proportional term for anti theft feature defined in per unit current per mechanical revolution	pu/rev	68
Lm	Motor magnetizing inductance (default 0)	uHenries	69
Rated system voltage	System voltage rating is the battery voltage	Volts	70
Rated motor current	Nameplate motor peak phase current rating	Amps	71
Rated motor speed	Nameplate no load rated motor RPM	RPM	72
Rated motor power	Motor rated electrical power = rated Vbattery * rated Ibattery	Watts	73
Ls	Motor phase to neutral stator inductance	uHenries	74
Rs	Motor phase to neutral stator resistance	mOhms	75
depricated Kv always 1	Motor back electromotive force constant that is equivalent to per unit system voltage/per unit rated speed	pu	76
Motor position sensor type	0 is hall based / 1 is hall start and sensorless run / 2 is sensorless / 3 is reserved		77
# of motor pole pairs	The motor's number of electrical pole pairs		78
Hall offset	Hall sensor offset angle	degrees	79
Hall sector[0]	Motor sector represented by Hall sequence 000 -1=illegal state		80
Hall sector[1]	Motor sector represented by Hall sequence 001		81
Hall sector[2]	Motor sector represented by Hall sequence 010		82
Hall sector[3]	Motor sector represented by Hall sequence 011		83
Hall sector[4]	Motor sector represented by Hall sequence 100		84
Hall sector[5]	Motor sector represented by Hall sequence 101		85
Hall sector[6]	Motor sector represented by Hall sequence 110		86
Hall sector[7]	Motor sector represented by Hall sequence 111 -1=illegal state		87
Hall interpolation start frequency	Electrical frequency to start interpolating the halls	Hertz	88
Hall interpolation stop frequency	Electrical frequency to stop interpolating the halls	Hertz	89
Motor over temperature trip threshold	Maximum motor temperature	deg C	90
Motor foldback starting temperature	Motor temperature at which output current foldback begins	deg C	91
Motor foldback ending temperature	Motor temperature at which output current is folded back to 0 Amperes	deg C	92
Temperature feedback V at 0 C	Temperature sensor's output voltage at 0 C	Volts	93
Temperature feedback V at 25 C	Temperature sensor's output voltage at 25 C	Volts	94
Temperature feedback V at 50 C	Temperature sensor's output voltage at 50 C	Volts	95
Temperature feedback V at 75 C	Temperature sensor's output voltage at 75 C	Volts	96
Temperature feedback V at 100 C	Temperature sensor's output voltage at 100 C	Volts	97
Temperature feedback V at 125 C	Temperature sensor's output voltage at 125 C	Volts	98
Overload continous current	Current as % of nameplate at which the motor can run without heating up	% rated	99
Overload heating current	Current as % of nameplate at which the motor will heat up to 100% over the heating time	% rated	100
Overload heating time	Time at which 100% heat is accumulated while operating at the Overload heating current	s	101
Overload cooling current	Current as % of nameplate at which the motor will cool to 0% over the cooling time	% rated	102
Overload cooling time	Time at which 100% heat is dissapated while operating at the Overload cooling current	s	103
Overload foldback start		%	104
Overload foldback end		%	105
Sensorless open loop starting current	Open loop sensorless AC current injection limit with respect to rated current	pu A	106
Sensorless open loop injection current ramp time	Duration of time it takes to reach Sensorless open loop starting current	ms	107
Sensorless closed loop enable frequency	Motor electrical frequency at which the transition from open loop to closed loop sensorless control occurs	Hertz	108
Sensorless open loop freq ramp time ms	Duration of time it takes to go from DC to the sensorless closed loop enable frequency	ms	109
Sensorless open loop dc current hold time	The length of time the controller maintain DC current in the motor windings during open loop start up	ms	110
Battery upper range	Battery highest range at minimum assist from motor	km	111
Display language and units	0=Dutch-km, 1=German-km, 2=ENGLISH-km, 3=English-km, 4=ENGLISH-mi		112
POD LED Brightness	1 is lowest, 20 is highest		113
BMS_abs_soc	BMS absolute SOC		114
BMS_rel_soc	BMS relative SOC		115
Single push assist source	0=brake 2, 1= brake 1, 2=cruise, 3=pfs		116
BMS_bat_voltage	BMS battery voltage		117
Single push boost time	time in s to keep boost enabled	s	118
Hall transitions to start free wheel	Number of Hall transitions to kick in free wheel		119
Battery lower range	Battery lower range at maximum assist from motor	km	120
PLL test 1	Test Variable for now		121
spare 13	Field weakening map current setpoint 4	% of rated motor current	122
spare 14	Field weakening map current setpoint 5	% of rated motor current	123
spare 15	Field weakening map current setpoint 6	% of rated motor current	124
spare 16	Field weakening map current setpoint 7	% of rated motor current	125
BlueTooth Test Register	Used in bluetooth test during EOL Testing	% of rated motor current	126
Motor features	15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0 1=enable 0=disable bit 0: Swap motor phase A and C bit 1: Fault tolerant hall( switch to sensorless) bit 2: Bottom bracket motor (varying gear ratio) bit 3: Overload I^2t on battery not motor bit 4: Reserved bit 5: Reserved bit 6: Reserved bit 7: Reserved bit 8: Reserved bit 9: Reserved bit 10: Reserved bit 11: Reserved bit 12: Reserved bit 13: Reserved bit 14: Reserved bit 15: Reserved		127
Hall Interpolation Transitions	number of hall transitions to start interpolating when above the interpolation frequency		128
Maximum Field Weakening current	If not zero, then this is the limit for automatic field weakening (the table is ignored)	%	129
Hall angle current correction	Hall correction angle at rated current	degrees	130
Alternate rated motor power	rated motor power in alternate speed/power limit mode	W	131
Pedalec sensorless open loop starting current	Pedalec start open loop sensorless AC current injection limit with respect to rated current	pu A	132
Pedalec sensorless open loop freq ramp time ms	Pedalec start duration of time it takes to go from DC to the sensorless closed loop enable frequency	ms	133
Pedalec sensorless closed loop enable frequency	Motor electrical frequency at which the transition from open loop to closed loop sensorless control occurs	Hertz	134
High battery state of charge foldback starting capacity	Battery state of charge reading where the regen current begins to foldback in order to protect the battery	% SOC	135
High battery state of charge foldback end capacity	Battery state of charge reading at which the regen is folded back to 0 Amperes	% SOC	136
Motor temperature source	Motor temperature sensor feedback source 0=brake 2, 1=brake 1, 2=bms, 3=throttle		137
Walk mode signal source	Walk mode signal source 0=cruise, 1=pfs, 2=brake 1, 3=brake 2, 4=serial(display)		138
Alternate power switch source	Alternate power switch signal source 0=cruise, 1=pfs, 2= brake 1, 3=brake 2, 4=remote pwr sw, 5=remote spd sw		139
Alternate speed limit switch source	Alternate speed limit switch signal source 0=cruise, 1=pfs, 2= brake 1, 3=brake 2, 4=remote pwr sw, 5=remote spd sw		140
Low battery foldback starting voltage	Battery voltage level at which output foldback begins in order to protect the battery	% of rated system voltage	141
Low battery foldback end voltage	Battery voltage level at which the output is folded back to 0 Amperes	% of rated system voltage	142
Cold battery foldback starting temperature	Battery temperature where the output current begins to foldback in order to protect the battery	deg C	143
Cold battery foldback ending temperature	Battery temperature at which the output is folded back to 0 Amperes	deg C	144
Low battery state of charge foldback starting capacity	Battery state of charge reading where the output current begins to foldback in order to protect the battery	% SOC	145
Low battery state of charge foldback end capacity	Battery state of charge reading at which the output is folded back to 0 Amperes	% SOC	146
Fast over voltage threshold	Instantaneous DC over voltage trip threshold will trigger a fault if an instantaneous or single voltage measurement greater than its current value as a percentage of Rated motor voltage. For example, if the Rated motor voltage = 48 Volts and the Fast over voltage threshold = 120%, then an over voltage fault will occur if the measured voltage exceeds 57.6 Volts.	% of rated system voltage	147
Fast under voltage threshold	Instantaneous DC under voltage trip threshold will trigger a fault if an instantaneous or single voltage measurement less than its current value as a percentage of rated motor voltage. For example, if the Rated motor voltage = 48 Volts and the Fast under voltage threshold = 50%, then an over voltage fault will occur if the measured voltage is less than 24 Volts.	% of rated system voltage	148
Slow over voltage threshold	Averaged DC over voltage trip threshold will trigger a fault if filtered voltage measurement greater than its current value as a percentage of Rated motor voltage. For example, if the Rated motor voltage = 48 Volts and the Slow over voltage threshold = 110%, then an over voltage fault will occur if the measured voltage exceeds 52.8 Volts.	% of rated system voltage	149
Slow under voltage threshold	Averaged DC under voltage trip threshold will trigger a fault if the filtered voltage measurement less than its current value as a percentage of rated motor voltage. For example, if the Rated motor voltage = 48 Volts and the Slow under voltage threshold = 75%, then an over voltage fault will occur if the measured voltage is less than 36 Volts.	% of rated system voltage	150
Throttle deadband threshold	Voltage value that is defines the amount of throttle travel between neutral and active throttle	Volts	151
Throttle fault range	Voltage added/subtracted to the throttle's measured high/low reading in order determine if the input is valid or not	Volts	152
Reserved L1 1	Reserved for future use		153
Maximum braking torque	Maxium braking torque limit as a function maximum motor current	% of rated motor current	154
Battery current limit	Maximum controller imposed battery current limit when motoring equal to rated motor power/rated system voltage	% of rated battery current	155
Regeneration battery current limit	Maximum controller imposed battery current limit when generating equal to rated motor power/rated system voltage	% of rated battery current	156
Power map Watts setpoint 1	Power map Wattage setpoint 1	% of rated power	157
Power map Watts setpoint 2	Power map Wattage setpoint 2	% of rated power	158
Power map Watts setpoint 3	Power map Wattage setpoint 3	% of rated power	159
Power map Watts setpoint 4	Power map Wattage setpoint 4	% of rated power	160
Power map Watts setpoint 5	Power map Wattage setpoint 5	% of rated power	161
Power map Watts setpoint 6	Power map Wattage setpoint 6	% of rated power	162
Power map Watts setpoint 7	Power map Wattage setpoint 7	% of rated power	163
Power map Watts setpoint 8	Power map Wattage setpoint 8	% of rated power	164
Power map speed setpoint 1	Power map speed setpoint 1	% of rated rpm	165
Power map speed setpoint 2	Power map speed setpoint 2	% of maximum speed	166
Power map speed setpoint 3	Power map speed setpoint 3	% of maximum speed	167
Power map speed setpoint 4	Power map speed setpoint 4	% of maximum speed	168
Power map speed setpoint 5	Power map speed setpoint 5	% of maximum speed	169
Power map speed setpoint 6	Power map speed setpoint 6	% of maximum speed	170
Power map speed setpoint 7	Power map speed setpoint 7	% of maximum speed	171
Power map speed setpoint 8	Power map speed setpoint 8	% of rated rpm	172
Minimum motoring torque	Torque setpoint at zero % throttle	pu A	173
Features2	15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0 1=enable 0=disable bit 0: Headlight Always ON enable bit 1: HDQ Replicating HALL bit 2: Free Wheel with no throttle bit 3: Reserved bit 4: Reserved bit 5: Reserved bit 6: Reserved bit 7: Reserved bit 8: Reserved bit 9: Invert Bit 9 of HW Config bit 10: Reserved bit 11: Reserved bit 12: Reserved bit 13: Reserved bit 14: Reserved bit 15: Reserved		174
Pedal speed map offset	Speed setpoint when the pedal rpm equals zero	pu	175
Pedal speed map end	Pedal rpm that equates to full gain	RPM	176
Engine braking torque	engine braking in % of full braking torque	%	177
Torque sensor symmetry	Defines symmetry or torque sensor for filtering. Left leg only sensors should be set to 0 to average the lack of right leg torque. 0=one cycle(default), 1=halfcycle, 2=quarter cycle		178
Torque sensor power gain	Scales pedal torque in Nm to throttle % as using the following equation: Throttle = 100%* T(Nm)*G(pu)/64	G	179
Torque sensor initial torque	Left leg only sensors can use this to compensate for the lack of an intial right leg torque	Nm	180
Torque sensor deadband torque	Negative saturation value for calculating average pedal torque; use negative number to correct for pedaling form	Nm	181
Pedal torque sensor offset voltage	Pedal torque sensor offset voltage has to be set by entering the sensor specification value or the measured throttle voltage when 0 torque is applied	Volts	182
Torque sensor voltage gain	Equates sensor output voltage to a torque measurement. This voltage gain can be found in the specifications for that sensor. Note: Some Thun sensors have a negative gain (-100Nm/Volt) while most other types are positive (voltage output goes up as pedal is pushed harder).	Nm/Volt	183
Datalog channel 1 select	Selection number = modbus address of the parameter/varialbe to be datalogged		184
Datalog channel 2 select	Selection number = modbus address of the parameter/varialbe to be datalogged		185
Datalog channel 3 select	Selection number = modbus address of the parameter/varialbe to be datalogged		186
Datalog channel 4 select	Selection number = modbus address of the parameter/varialbe to be datalogged		187
Datalog trigger level	Oscilloscope's trigger level as a signed int.		188
Datalog trigger mask	Mask for bit values; use 0xFFFF to disable		189
Datalog hold off	Number of samples before trigger		190
Datalog timebase	Number of ISRs per sample		191
Datalog trigger mode	0 is rising / 1 is falling / 2 is equal to / 3 is not equal to		192
Wheel speed sensor source	0 is cruise / 1 is brake 2 / 2 is Hall A		193
High battery foldback starting voltage	Battery voltage level at which output foldback begins in order to protect the battery	% of rated system voltage	194
High battery foldback end voltage	Battery voltage level at which the output is folded back to 0 Amperes	% of rated system voltage	195
Low battery state of charge alarm threshold	Low battery state of charge alarm threshold	%	196
Voltage model battery state of charge gain	% state of charge change for 1pu battery voltage change	%	197
Voltage model battery state of charge offset	% state of charge offset value	%	198
Axle torque sensor assist 1	torque sensor gain multiplier for assist mode1 (only for Assist mode source = 0 or 8)	pu	199
Axle torque sensor 2	torque sensor gain multiplier for assist mode2 (only for Assist mode source = 0 or 8)	pu	200
Axle torque sensor 3	torque sensor gain multiplier for assist mode 3 (only for Assist mode source = 0 or 8)	pu	201
Rolling start speed 1	Starting speed for assist mode 1	km/hr	202
Rolling start speed 2	Starting speed for assist mode 2	km/hr	203
Rolling start speed 3	Starting speed for assist mode 3	km/hr	204
Rolling start speed	Starting speed	km/hr	205
Regen brake speed	Minimum speed for regen brake	km/hr	206
Stromer ST1 Display Configuration	ST1 Display Configuration. Format: 0x ValueB:ValueA ValueA = F6 (USA/CH), or EE (EU) ValueB = 86	hex	207
Control command source	0 is serial stream / 1 is throttle / 2 is pedal sensor / 3 is throttle AND pedal sensor / 4 is throttle OR pedal sensor /5 is obsolete (old torque sensor, see pedal sensor)		208
Battery management interface type	0 is none / 1 is voltage model / 2 is analog 10V / 3 is reserved / 4 is LIN / 5 is ModBus. If None is selected the SOC will always read 100%. Other voltage parameters should be configured to protect the system		209
Assist mode source	0=none, 1=analog, 2=Display, 3=ASI 485 Display, 4=obsolete, 5=network gains, 6=reserved, 7=ASI LIN Pod		210
Pedal sensor type	0 is single Hall / 1 is dual Hall / 2 is FAG / 3 is Quadrature torque / 4 is Quadrature speed / 5 is Axle torque / 6 is single hall reverse		211
Features	15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0 1=enable 0=disable bit 0: Reserved bit 1: Reverse enable on cruise bit 2: Anti theft on pfs bit 3: Reserved bit 4: Analogue braking enable bit 5: Motor temperature sensor enable bit 6: Motor shutoff on stall enable bit 7: Reverse interlock disable bit 8: Alternate speed limit enable bit 9: Rolling start enable bit 10: Alternate power limit enable bit 11: Walk mode enable bit 12: Boost mode enable bit 13: Engine braking enable bit 14: Ext Fault LED on HQD bit 15: Reserved		212
Throttle full voltage	Throttle voltage reading with the throttle open (fully on)	Volts	213
Throttle off voltage	Throttle voltage reading with the throttle closed (fully off)	Volts	214
Analogue brake full voltage	Analog brake voltage reading that equates to the maximum brake setpoint	Volts	215
Analogue brake off voltage	Analog brake voltage reading that equates to the brake being off	Volts	216
Assist high voltage reading	Assist voltage reading when high level assist is selected	Volts	217
Assist low voltage reading	Assist voltage reading when low level assist is selected	Volts	218
Assist gain 1	Fraction of maximum power at lowest assist level (assist 1)	pu	219
Positive motoring torque ramp	Time required to reach the maximum motoring torque setpoint	ms	220
Negative motoring torque ramp	Time required to reach the zero motoring torque	ms	221
Pedalec positive motoring torque ramp	Time required to reach the maximum motoring torque setpoint for pedal sensors	ms	222
Pedalec negative motoring torque ramp	Time required to reach the zero motoring torque for pedal sensors	ms	223
Positive braking torque ramp	Time required to reach the maximum braking torque setpoint	ms	224
Negative braking torque ramp	Time required to reach the zero braking torque	ms	225
Gear ratio	Ratio of motor revolutions to one wheel revolution	N:1	226
Wheel diameter	Wheel diameter in mm	mm	227
Assist cut out distance	Maximum distance the bike is allowed to travel and provide assist power to the wheel after pedal activity has ceased	m	228
Vehicle maximum speed	Vehicle speed limit for foldback in km/hr	km/hr	229
Vehicle jog speed	Vehicle speed limit for jog mode in km/hr	km/hr	230
Wheel speed sensor pulses per revolution	Represents the wheel speed sensor's number of pulses per wheel revolution. 0 disables this feature	ppr	231
Pedalec minimum timeout	Minimum time to disable pedal when no change is position is noticed	ms	232
Pedalec maximum timeout	Maximum time to disable pedal when no change is position is noticed	ms	233
Pedal speed sensor pulses per revolution	Represents the pedal speed sensor's number of pulses per revolution.	ppr	234
Pedal sense delay	Represents the number of pedal speed pulses that must be observed before the pedals are deemed to be active	counts	235
Vehicle maximum speed 2	Secondary vehicle speed limit for foldback in km/hr	km/hr	236
Reserved L1 6	Reserved for future use		237
Reserved L1 7	Reserved for future use		238
Reserved L1 8	Reserved for future use		239
Reserved L1 9	Reserved for future use		240
Assist speed 1	Fraction of maximum speed at lowest assist level (assist 1)	pu	241
Reserved L1 3	Reserved for future use		242
Reserved L1 4	Reserved for future use		243
Reserved L1 5	Reserved for future use		244
Assist gain 2	Fraction of maximum power at intermediate assist levels. For 9 levels of assist this is actually level 5. For 5 levels of assist this is actually level 3. For 3 levels of assist this is actually levels 2. For 4 levels of assist this is actually level 2.	pu	245
Assist speed 2	Fraction of maximum speed at intermediate assist levels. For 9 levels of assist this is actually level 5. For 5 levels of assist this is actually level 3. For 3 levels of assist this is actually levels 2. For 4 levels of assist this is actually level 2.	pu	246
Throttle sensor source	0= Throttle Voltage, 1=brake 1, 2=brake 2, 3=CAN torque, 4=LIN, 5=Network Voltage, 6=10V bms in		247
Cutoff brake sensor source	0=brake 1, 1=brake 2, 2=PFS, 3=cruise, 4=Network		248
Regen brake source	0=brake 2, 1= brake 1, 2=network, 3=ASI		249
Assist Gain 3	Used only for single switch assist option. Fraction of maximum power at assist level 3 of 4	pu	250
Assist Speed 3	Used only for single switch assist option. Fraction of maximum speed at assist level 3 of 4	pu	251
Vehicle jog speed2	Vehicle speed limit for boost mode, and inhibit speed for anti theft in km/hr	km/hr	252
Assist Gain Walk	Gain for walk mode		253
Speed limit ramp time	Speed limit ramp time for smooth clutch engagement on freewheel motors, 0 = disable	ms	254
CAN sync loss timeout	timeout for CAN systems when no sync pulses are recieved	ms	255
software revision level	Software revision level		256
controller status	TBD		257
faults	15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0 1=active 0=not active bit 0: Controller over voltage (flash code 1,1) bit 1: Phase over current (flash code 1,2) bit 2: Current sensor calibration (flash code 1,3) bit 3: Current sensor over current (flash code 1,4) bit 4: Controller over temperature (flash code 1,5) bit 5: Motor Hall sensor fault (flash code 1,6) bit 6: Controller under voltage (flash code 1,7) bit 7: POST static gating test (flash code 1,8) bit 8: Network communication timeout (flash code 2,1) bit 9: Instantaneous phase over current (flash code 2,2) bit 10: Motor over temperature (flash code 2,3) bit 11: Throttle voltage outside range (flash code 2,4) bit 12: Instantaneous controller over voltage (flash code 2,5) bit 13: Internal error (flash code 2,6 bit 14: POST dynamic gating test (flash code 2,7) bit 15: Instantaneous under voltage (flash code 2,8)		258
controller temperature	Base plate temperature	deg C	259
vehicle speed	Calculated vehicle speed	km/hr	260
motor temperature	Motor temperature	deg C	261
motor current	Motor peak current	Amps	262
motor rpm	Motor speed	RPM	263
motor speed	Motor speed	% of rated rpm	264
battery voltage	Measured battery voltage	Volts	265
battery current	Measured battery amperage	Amps	266
battery state of charge	Remaining battery capacity	%	267
battery power	Calculated battery output power	Watts	268
last fault	15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0 1=active 0=not active bit 0: Controller over voltage (flash code 1,1) bit 1: Phase over current (flash code 1,2) bit 2: Current sensor calibration (flash code 1,3) bit 3: Current sensor over current (flash code 1,4) bit 4: Controller over temperature (flash code 1,5) bit 5: Motor Hall sensor fault (flash code 1,6) bit 6: Controller under voltage (flash code 1,7) bit 7: POST static gating test (flash code 1,8) bit 8: Network communication timeout (flash code 2,1) bit 9: Instantaneous phase over current (flash code 2,2) bit 10: Motor over temperature (flash code 2,3) bit 11: Throttle voltage outside range (flash code 2,4) bit 12: Instantaneous controller over voltage (flash code 2,5) bit 13: Internal error (flash code 2,6) bit 14: POST dynamic gating test (flash code 2,7) bit 15: Instantaneous under voltage (flash code 2,8)		269
throttle voltage	Filtered throttle voltage	Volts	270
brake 1 voltage	Filtered brake 1 voltage	Volts	271
brake 2 voltage	Filtered brake 2 voltage	Volts	272
raw controller temperature sensor voltage	Unfiltered controller temperature sensor voltage	Volts	273
light sensor voltage	Filtered light sensor voltage	Volts	274
analog bms soc voltage	Filtered BMS voltage	Volts	275
digital inputs	9 8 7 6 5 4 3 2 1 0 1=logic high 0=logic low bit 0: Hall C bit 1: Hall B bit 2: Hall A bit 3: Pedal First input bit 4: Cruise input bit 5: Brake 1 input bit 6: Brake 2 input bit 7: HWOC Pin bit 8: HWOC Latch bit 9: Remote Brake bit 10: Remote Pwr Rating Sw bit 11: Remote Regen1 bit 12: Remote Regen2 bit 13: Remote Spd Rating Sw		276
warnings	7 6 5 4 3 2 1 0 1=active 0=not active bit 0: Communication Timeout (flash code 5,1) bit 1: Hall Sensor (flash code 5,2) bit 2: Hall stall (flash code 5,3) bit 3: Wheel Speed Sensor(flash code 5,4) bit 4: CAN Bus (flash code 5,5) bit 5: Hall Illegal sector (flash code 5,6) bit 6: Hall illegal transition (flash code 5,7) bit 7: VdcLowFLDBK (flash code 5,8) bit 8: VdcHighFLDBK (flash code 6,1) bit 9: MotorTempFLDBK (flash code 6,2) bit 10: ContrlTempFLDBK (flash code 6,3) bit 11: LowSOCFLDBK (flash code 6,4) bit 12: HiSOCFLDBK (flash code 6,5) bit 13: I2tFLDBK (flash code 6,6) bit 14: (flash code 6,7) bit 15: BMSTimeout(flash code 6,8)		277
rotor angle	Motor electrical position	degrees	278
battery temperature	battery temperature		279
battery power percent	battery power in W divided by rated power in W	% of rated power	280
dsp core temperature	DSP temperature	deg C	281
phase A current	Measured motor phase A current	Amps	282
phase B current	Calculated motor phase B current	Amps	283
phase C current	Measured motor phase C current	Amps	284
phase A voltage	Measured instantaneous motor phase A voltage	Volts	285
phase B voltage	Measured instantaneous motor phase B voltage	Volts	286
phase C voltage	Measured instantaneous motor phase C voltage	Volts	287
boot loader software revision	Bootloader software revision		288
light supply voltage	6V light supply voltage for headlight brake light and running light	V	289
high state of charge foldback gain	high state of charge foldback on battery regen current		290
raw battery voltage	Unfiltered battery voltage measurement	pu V	291
phase A voltage per unit	Instantaneous phase A voltage measurement	pu V	292
phase B voltage per unit	Instantaneous phase B voltage measurement	pu V	293
phase C voltage per unit	Instantaneous phase C voltage measurement	pu V	294
digital outputs	15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0 1=active 0=not active bit 0: Headlight bit 1: RS 485 TX bit 2: HDQ TX bit 3: Current sensor power bit 4: Main power bit 5: LED bit 6: Hardware over current reset bit 7: A bit 8: B bit 9: C bit 10: Running light bit 11: Brake light bit 12: LIN enable bit 13: FAG enable bit 14: Charger disable bit 15:		295
ia_pu	Reserved for future use		296
ic_pu	Reserved for future use		297
overload accumulator	Accumulated i^2t overload heat in %	%	298
faults2	15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0 1=active 0=not active bit 0: Parameter CRC (flash code 3,1) bit 1: Current Scaling(flash code 3,2) bit 2: Voltage Scaling(flash code 3,3) bit 3: Headlight Undervoltage(flash code 3,4) bit 4: Torque sensor(flash code 3,5) bit 5: CAN bus(flash code 3,6) bit 6: Hall Stall(flash code 3,7) bit 7: Bootloader(flash code 3,8) bit 8: Parameter2CRC(flash code 4,1) bit 9: (flash code 4,2) bit 10: (flash code 4,3) bit 11: (flash code 4,4) bit 12:(flash code 4,5) bit 13: (flash code 4,6) bit 14: (flash code 4,7) bit 15: (flash code 4,8)		299
motor phase U high voltage POST	Measured phase U voltage at 85% duty cycle nomalized to the battery voltage	V (norm)	300
motor phase U low voltage POST	Measured phase U voltage at 15% duty cycle nomalized to the battery voltage	V (norm)	301
motor phase V high voltage POST	Measured phase V voltage at 85% duty cycle nomalized to the battery voltage	V (norm)	302
motor phase V low voltage POST	Measured phase V voltage at 15% duty cycle nomalized to the battery voltage	V (norm)	303
motor phase W high voltage POST	Measured phase W voltage at 85% duty cycle nomalized to the battery voltage	V (norm)	304
motor phase W low voltage POST	Measured phase W voltage at 15% duty cycle nomalized to the battery voltage	V (norm)	305
motor phase U open circuit voltage POST	Measured phase U open circuit voltage nomalized to the battery voltage	V (norm)	306
motor phase V open circuit voltage POST	Measured phase V open circuit voltage nomalized to the battery voltage	V (norm)	307
motor phase W open circuit voltage POST	Measured phase W open circuit voltage nomalized to the battery voltage	V (norm)	308
phase regen current power limit	motor phase current limit due to power or battery current	pu	309
high voltage foldback gain	battery limit high voltage foldback gain	pu	310
wheel RPM (speed sensor based)	Calculated wheel speed based on wheel speed sensor	RPM	311
wheel RPM (motor based)	Calculated wheel speed based on motor pole pairs	RPM	312
measured wheel RPM	Measured wheel speed	RPM	313
local power limit command	switched between 1.0 and ratio of alt rated power	pu	314
phase A current sensor offset	% of full scale sensor reading (nominal value = 0.5)	% of full scale	315
phase C current sensor offset	% of full scale sensor reading (nominal value = 0.5)	% of full scale	316
low voltage foldback gain	battery low voltage foldback gain	pu	317
phase motoring current power limit	motor phase current limit due to power or battery current	pu	318
motor i^2t foldback gain	Motor I^2t overload foldback gain	pu	319
motor temperature foldback gain	Motor temperature foldback gain	pu	320
inverter temperature foldback gain	Inverter (hot and cold) foldback gain	pu	321
speed limiter output	Current limit due to speed (speed reg mode 2 only)	pu	322
motoring phase current limit	Maximum motor current after thermal foldbacks applied	pu	323
low state of charge foldback gain	Battery low state of change foldback gain	pu	324
throttle setpoint	Filtered throttle signal	pu	325
brake setpoint	Filtered analog brake	pu	326
ebike flags	11 10 9 8 7 6 5 4 3 2 1 0 1=active 0=not active bit 0: Brake bit 1: Cutout bit 2: Run Req bit 3: Pedal bit 4: Regen bit 5: Walk bit 6: Walk start bit 7: Throttle bit 8: Rvs bit 9: Interlock off bit 10: Pedal ramp rate active bit 11: Gate enble request bit 12: Gate enabled bit 13: Boost mode bit 14: Anti theft enabled		327
instantaneous pedal speed	instantaneous pedal speed	RPM	328
assist speed limit	Speed limit reduction based on assist mode	pu	329
sensorless state	Defines current state of sensorless startup state machine		330
average pedal speed	Measured pedal speed in RPM from pedal sensor	RPM	331
average pedal torque	Measured pedal torque in Nm from pedal sensor	Nm	332
regen phase current limit	Maximum motor regen current after thermal foldbacks applied	pu	333
motor input power	Motor input power in Watts	W	334
torque command	Requested motor torque from sensors before rate limiting	pu	335
torque reference	Requested motor torque after rate limiting	pu	336
speed(ref/limit) command	Speed limit in local mode	pu	337
pedal speed gain	Pedal speed gain	pu	338
assist level	Assist level	pu	339
modbus1 CRC error count	Number of ModBus CRC errors since power-up or reset on port1.	counts	340
modbus1 HW errors	Number of UART errors since power-up or reset on port1.	counts	341
modbus2 CRC error count	Number of ModBus CRC errors since power-up or reset on port2.	counts	342
modbus2 HW errors	Number of UART errors since power-up or reset on port2.	counts	343
reserved L4 4	reserved for future use	counts	344
vd	Filtered D axis voltage	pu	345
vq	Filtered Q axis voltage	pu	346
d feedback avg	Filtered D axis current	pu	347
q feedback avg	Filtered Q axis current	pu	348
Axle torque sensor offset voltage	Axle torque sensor offset voltage power up calibration. This offset is calculated at power up instead of using the Pedal torque sensor offset when the Pedal senosr type is set to Axle Torque Sensor	V	349
current ISR execution time	Measured ISR execution time	us	350
peak ISR execution time	Peak ISR execution time	us	351
peak 1ms loop time	Measured execution time	us	352
average 1ms time	Measured execution time	us	353
1ms time	Measured execution time	us	354
execution time 4	Measured execution time	us	355
execution time 5	Measured execution time	us	356
execution time 6	Measured execution time	us	357
execution time 7	Measured execution time	us	358
execution time 8	Measured execution time	us	359
execution time 9	Measured execution time	us	360
execution time 10	Measured execution time	us	361
execution time 11	Measured execution time	us	362
custom code crc high	High word of the 32 bit CRC calculation of the custom code		363
custom code crc low	Low word of the 32 bit CRC calculation of the custom code		364
custom code execution time	Measured execution time	us	365
v integral	Speed regulator integral term	pu	366
v output	Speed regulator output	pu	367
v error	Speed regulator error term	pu	368
v proportional	Speed regulator proportional term	pu	369
d integral	D axis current loop integral term	pu	370
q integral	Q axis current loop integral term	pu	371
d output	D axis current loop output	pu	372
q output	Q axis current loop output	pu	373
d error	D axis current loop error term	pu	374
q error	Q axis current loop error term	pu	375
d proportional	D axis current loop proportional term	pu	376
q proportional	Q axis current loop proportional term	pu	377
q limit from d	q axis limit based on d axis	pu	378
battery i^2t foldback gain	battery I^2t overload foldback gain	pu	379
d feedback	D axis current loop feedback	pu	380
q feedback	Q axis current loop feedback	pu	381
d reference	D axis current loop reference	pu	382
q reference	Q axis current loop reference	pu	383
maximum measurable current		A	384
maximum measurable voltage		V	385
positive battery limit	motoring battery current limit after battery foldbacks	pu	386
negative battery limit	regen battery current limit after battery foldbacks	pu	387
stator current alpha	Stationary alpha axis rotor current (Factory only)	pu	388
stator current beta	Stationary beta axis rotor current (Factory only)	pu	389
flux alpha	Flux model phase Alpha output	pu	390
flux beta	Flux model phase Beta output	pu	391
flux frequency	Frequency of flux model	Hertz	392
flux magnitude	Magnitude of flux	pu	393
flux angle	Angle of flux	pu	394
open loop angle	Open loop mode angle	deg	395
calculated battery current motoring limit	Effective motoring battery current limit	A	396
calculated battery current braking limit	Effective braking battery current limit	A	397
motor temperature sensor voltage	Motor temperature sensor voltage at the A/D converter to compare with the table.	V	398
pu Lm	per unit magnetizing inductance	pu	399
debug1	Debug variable for general development use		400
debug2	Debug variable for general development use		401
debug3	Debug variable for general development use		402
POD switch value	15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0 1=enabled 0=disabled bit 0: POD Top Button bit 1: POD Middle Button bit 2: POD Bottom Button bit 3: bit 4: bit 5: bit 6: bit 7: bit 8: bit 9: bit 10: bit 11: bit 12: bit 13: bit 14: bit 15:		403
LIN odometer	LIN network POD odometer distance (units defined in language selection)		404
LIN trip	LIN network POD trip distance(units defined in language selection)		405
LIN average trip velocity	LIN network average trip velocity(units defined in language selection)		406
wheel pulse counter	wheel pulse counter		407
trip meter	distance travelled in km since power up	km	408
pedalec_timeout_delay	calculated pedalec_timeout_delay from speed and stop distance		409
pll angle	Phase locked loop angle	pu	410
pll error	Phase locked loop error term	pu	411
pll PI frequency	Phase locked loop PI frequency	Hertz	412
pll proportional	Phase locked loop proportional term	Hertz	413
pll integral	Phase locked loop intergral term	Hertz	414
rotor frequency	Rotor's electrical frequency of rotation	Hertz	415
pll reference angle	Phase locked loop reference angle	pu	416
hall angle	Motor Hall angle	pu	417
last fault2	15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0 1=active 0=not active bit 0: Parameter CRC bit 1: Current Scaling bit 2: Voltage Scaling bit 3: Headlight Undervoltage bit 4: Torque sensor bit 5: CAN bus bit 6: Hall Stall bit 7: bit 8: bit 9: bit 10: bit 11: bit 12: bit 13: bit 14: bit 15:		418
hall frequency	Hall signal frequency	Hertz	419
q limit			420
d limit			421
id ref trim			422
id ref fdfwd			423
autotune Lm	Autotuned value for magnetizing inductance as calculated by the autotune motor parameter test	uHenries	424
autotune Rs	Stator winding resistance as calculated by the autotune motor parameter test	mOhms	425
autotune Ls	Stator winding inductance as calculated by the autotune motor parameter test	uHenries	426
pu Rs	Per unit stator line to neutral stator resistance (factory use only)	pu mohm	427
pu Ls	Per unit stator line to neutral stator inductance (factory use only)	pu uHenries	428
rated electrical frequency	The rated electrical commutation frequency = Npolepairs*Rated_rpm/60	Hz	429
spare var 7	(factory use only)	pu	430
spare var 8	(factory use only)	pu	431
spare var 9	(factory use only)	pu	432
Ia_rms	phase a rms current for calibration	Arms	433
Ic_rms	phase c rms current for calibration	Arms	434
Iq_trim_q12	(factory use only)	pu	435
modulation index	(factory use only)		436
pwm cmd a pwm	(Factory only)		437
pwm cmd b pwm	(Factory only)		438
pwm cmd c pwm	(Factory only)		439
autotune hall sector[0]	Output of the auto tune hall sequence test for sector [0]		440
autotune hall sector[1]	Output of the auto tune hall sequence test for sector [1]		441
autotune hall sector[2]	Output of the auto tune hall sequence test for sector [2]		442
autotune hall sector[3]	Output of the auto tune hall sequence test for sector [3]		443
autotune hall sector[4]	Output of the auto tune hall sequence test for sector [4]		444
autotune hall sector[5]	Output of the auto tune hall sequence test for sector [5]		445
autotune hall sector[6]	Output of the auto tune hall sequence test for sector [6]		446
autotune hall sector[7]	Output of the auto tune hall sequence test for sector [7]		447
parameter CRC32 high word	High word of the 32 bit CRC calculation of the parameters		448
parameter CRC32 low word	Low word of the 32 bit CRC calculation of the parameters		449
user access level	Current user parameter access level		450
bootloader CRC32 high word	High word of the 32 bit CRC calculation of the bootloader		451
bootloader CRC32 low word	Low word of the 32 bit CRC calculation of the bootloader		452
application CRC32 high word	High word of the 32 bit CRC calculation of the application software		453
application CRC32 low word	Low word of the 32 bit CRC calculation of the application software		454
Silicon Revision	Reserved for factory use		455
execution time 15	Reserved for future use		456
check execution time 16	Reserved for future use	us	457
peak background period	Reserved for future use	us	458
avg background period	Reserved for future use	us	459
autotune hall offset angle	estimated hall offset angle	degrees	460
depricated autotune Kv always 1	Motor back electromotive force constant that is equivalent to per unit system voltage/per unit rated speed	pu	461
autotune rated rpm	Nameplate no load rated motor RPM	RPM	462
Axle torque sensor assist	Axle torque sensor multiplier for assist mode	pu	463
rolling start speed	rolling start speed for assist mode	km/hr	464
OTP serial number0	Reserved for factory use		465
OTP serial number1	Reserved for factory use		466
OTP serial number2	Reserved for factory use		467
OTP serial number3	Reserved for factory use		468
OTP serial number4	Reserved for factory use		469
OTP serial number5	Reserved for factory use		470
OTP serial number6	Reserved for factory use		471
OTP serial number7	Reserved for factory use		472
Speed command	Speed command scaled a % of rated motor speed (used in networked configuration only)	% of rated rpm	473
Maximum motoring current	Maximum motoring current limit scaled a % of rated rated motor current (from local or remote VCM)	% of rated motor current	474
Maximum braking current	Maximum braking current limit scaled a % of rated rated motor current (from local or remote VCM)	% of rated motor current	475
State command	State command where 0=OFF, 1=IDLE, 2=RUN (used in networked configuration only)		476
Torque command	Torque command scaled a % of rated motor current (used in networked configuration only)	%	477
Running Light PWM (Daylight)	0 to 100%	%	478
Brake Light PWM (Daylight)	0 to 100%	%	479
Test mode	0 is closed loop current mode (standard operating mode) / 2 is open loop voltage mode / 3 is open loop current mode		480
Motor discover mode	0 is off / 1 is motor stationary parameter discover / 2 is moving parameter discover		481
Open loop modulation	Per unit modulation current/voltage	pu	482
Open loop current	Open loop current injection mode setpoint	Amps	483
Open loop frequency	Frequency of open loop current/voltage injection (if open loop angle is zero)	Hertz	484
Open loop angle	Open loop static electrical angle (over-rides frequency setpoint)	degrees	485
debug_cmd1	Reserved for future use		486
debug_cmd2	Reserved for future use		487
ebike flags2	11 10 9 8 7 6 5 4 3 2 1 0 1=active 0=not active bit 0: Regen Always without analog input bit 1: bit 2: bit 3: bit 4: bit 5: bit 6: bit 7: bit 8: bit 9: bit 10: bit 11: bit 12: bit 13: bit 14:		488
LIN network cmmd	Command to Lin Network devices 0=none, 1=POD bootload, 2=Display bootload, 3=Reset Trip, 4=Reset Odometer, 5=Bms bootload		489
Remote speed command	Speed command scaled a % of rated motor speed (only used if command control source = serial)	% of rated rpm	490
Remote maximum motoring current	Maximum motoring current limit scaled a % of rated rated motor current (only used if command control source = serial)	%	491
Remote maximum braking current	Maximum braking current limit scaled a % of rated rated motor current (only used if command control source = serial)	%	492
Remote state command	State command where 0=OFF, 1=IDLE and 2=RUN (only used if command control source = serial)		493
Remote torque command	Torque command scaled a % of rated motor xxxx (only used if command control source = serial)	%	494
Remote Throttle Voltage	Networked throttle voltage	Volts	495
Remote Digital Commands	9 8 7 6 5 4 3 2 1 0 1=active 0=not active bit 0: Cut out bit 1: HeadLight bit 2: RunLight bit 3: BrkLight bit 4: ChrgDisable bit 5: Alt Spd bit 6: Alt Pwr bit 7: Regen1 bit 8: Regen2 bit 9: HDQ		496
Remote Analog brake voltage	for remote analog brake levers on a display	V	497
Parameter read access code	enter code here to enable reading of parameters		498
Bidirectional torque command	positive for motoring, zero for idle negative for braking		499
Display speed limit command	Fraction of maximum speed when using a display based assist mode	pu	500
Display assist level command	Fraction of maximum assist level when using a display based assist mode	pu	501
Display walk command			502
Remote battery SOC	state of charge from modbus from remote bms		503
Remote battery temperature	battery temperature from BMS	C	504
Remote light sensor voltage	light sensor voltage from display	V	505
Remote assist mode	assist levels from display, values from 0 to 9 depending on display type		506
Arm datalogger	Set to 1 to arm the built in scope. Reports 2 if stopped		507
Fault clear	Write a nonzero value to clear fault		508
Parameter access code	This hex code determines which level of parameters the user has access to		509
Load firmware to flash	Set to 0x7FFF to load new application software		510
Write parameters to flash	Set to 0x7FFF to save parameters to flash. 0x3FFF to burn serial number to OTP. Returns 0x1000 if OK or 0x2000 if fail.		511
ptable1	ptable test		1536
ptable2	ptable test		1537
ptable3	ptable test		1538
ptable4	ptable test		1539
ptable5	ptable test		1540
ptable6	ptable test		1541
ptable7	ptable test		1542
ptable8	ptable test		1543
ptable9	ptable test		1544
ptable10	ptable test		1545
LIN_Frame ID	LIN Frame ID (with parity)	hex	1664
LIN Data Length	LIN Message number of data bytes	hex	1665
LIN_DATA_0	Generic LIN Packet, Data byte 0.	hex	1666
LIN_DATA_1	Generic LIN Packet, Data byte 1.	hex	1667
LIN_DATA_2	Generic LIN Packet, Data byte 2.	hex	1668
LIN_DATA_3	Generic LIN Packet, Data byte 3.	hex	1669
LIN_DATA_4	Generic LIN Packet, Data byte 4.	hex	1670
LIN_DATA_5	Generic LIN Packet, Data byte 5.	hex	1671
LIN_DATA_6	Generic LIN Packet, Data byte 6.	hex	1672
LIN_DATA_7	Generic LIN Packet, Data byte 7.	hex	1673
RPDO1 map1 sub index and size	RPDO1 map1 sub index (high byte) and size in bits (low bit)	hex	1792
RPDO1 map1 index	RPDO1 map1 index	hex	1793
RPDO1 map2 sub index and size	RPDO1 map2 sub index (high byte) and size in bits (low bit)	hex	1794
RPDO1 map2 index	RPDO1 map2 index	hex	1795
RPDO1 map3 sub index and size	RPDO1 map3 sub index (high byte) and size in bits (low bit)	hex	1796
RPDO1 map3 index	RPDO1 map3 index	hex	1797
RPDO1 map4 sub index and size	RPDO1 map4 sub index (high byte) and size in bits (low bit)	hex	1798
RPDO1 map4 index	RPDO1 map4 index	hex	1799
RPDO1 size (words)	RPDO1 size in words		1800
RPDO1 transmission type	asynchronous only (0 to disable, N to enable)		1801
RPDO1 timeout	RPDO1 timeout in ms (0 to disable)	ms	1802
parameters2 spare1	(not used)		1803
RPDO2 map1 sub index and size	RPDO2 map1 sub index (high byte) and size in bits (low bit)	hex	1804
RPDO2 map1 index	RPDO2 map1 index	hex	1805
RPDO2 map2 sub index and size	RPDO2 map2 sub index (high byte) and size in bits (low bit)	hex	1806
RPDO2 map2 index	RPDO2 map2 index	hex	1807
RPDO2 map3 sub index and size	RPDO2 map3 sub index (high byte) and size in bits (low bit)	hex	1808
RPDO2 map3 index	RPDO2 map3 index	hex	1809
RPDO2 map4 sub index and size	RPDO2 map4 sub index (high byte) and size in bits (low bit)	hex	1810
RPDO2 map4 index	RPDO2 map4 index	hex	1811
RPDO2 size (words)	RPDO2 size in words		1812
RPDO2 transmission type	asynchronous only (0 to disable, N to enable)		1813
RPDO2 timeout	RPDO2 timeout in ms (0 to disable)	ms	1814
parameters2 spare2	(not used)		1815
TPDO1 map1 sub index and size	TPDO1 map1 sub index (high byte) and size in bits (low bit)	hex	1816
TPDO1 map1 index	TPDO1 map1 index	hex	1817
TPDO1 map2 sub index and size	TPDO1 map2 sub index (high byte) and size in bits (low bit)	hex	1818
TPDO1 map2 index	TPDO1 map2 index	hex	1819
TPDO1 map3 sub index and size	TPDO1 map3 sub index (high byte) and size in bits (low bit)	hex	1820
TPDO1 map3 index	TPDO1 map3 index	hex	1821
TPDO1 map4 sub index and size	TPDO1 map4 sub index (high byte) and size in bits (low bit)	hex	1822
TPDO1 map4 index	TPDO1 map4 index	hex	1823
TPDO1 size (words)	TPDO1 size in words		1824
TPDO1 transmission type	TPDO1 number of syncs per transmission 0 to 240 (0 to disable, N for every Nth sync)		1825
TPDO1 event time	TPDO1 event time in ms for async tpdos (0 to disable)	ms	1826
TPDO1 sync window	TPDO1 sync window (not used)		1827
TPDO2 map1 sub index and size	TPDO2 map1 sub index (high byte) and size in bits (low bit)	hex	1828
TPDO2 map1 index	TPDO2 map1 index	hex	1829
TPDO2 map2 sub index and size	TPDO2 map2 sub index (high byte) and size in bits (low bit)	hex	1830
TPDO2 map2 index	TPDO2 map2 index	hex	1831
TPDO2 map3 sub index and size	TPDO2 map3 sub index (high byte) and size in bits (low bit)	hex	1832
TPDO2 map3 index	TPDO2 map3 index	hex	1833
TPDO2 map4 sub index and size	TPDO2 map4 sub index (high byte) and size in bits (low bit)	hex	1834
TPDO2 map4 index	TPDO2 map4 index	hex	1835
TPDO2 size (words)	TPDO2 size in words		1836
TPDO2 transmission type	TPDO2 number of syncs per transmission 0 to 240 (0 to disable, N for every Nth sync)		1837
TPDO2 event time	TPDO2 event time in ms for async tpdos (0 to disable)	ms	1838
TPDO2 sync window	TPDO2 sync window (not used)		1839
TPDO3 map1 sub index and size	TPDO3 map1 sub index (high byte) and size in bits (low bit)	hex	1840
TPDO3 map1 index	TPDO3 map1 index	hex	1841
TPDO3 map2 sub index and size	TPDO3 map2 sub index (high byte) and size in bits (low bit)	hex	1842
TPDO3 map2 index	TPDO3 map2 index	hex	1843
TPDO3 map3 sub index and size	TPDO3 map3 sub index (high byte) and size in bits (low bit)	hex	1844
TPDO3 map3 index	TPDO3 map3 index	hex	1845
TPDO3 map4 sub index and size	TPDO3 map4 sub index (high byte) and size in bits (low bit)	hex	1846
TPDO3 map4 index	TPDO3 map4 index	hex	1847
TPDO3 size (words)	TPDO3 size in words		1848
TPDO3 transmission type	TPDO3 number of syncs per transmission 0 to 240 (0 to disable, N for every Nth sync)		1849
TPDO3 event time	TPDO3 event time in ms for async tpdos (0 to disable)	ms	1850
TPDO3 sync window	TPDO3 sync window (not used)		1851
TPDO4 map1 sub index and size	TPDO4 map1 sub index (high byte) and size in bits (low bit)	hex	1852
TPDO4 map1 index	TPDO4 map1 index	hex	1853
TPDO4 map2 sub index and size	TPDO4 map2 sub index (high byte) and size in bits (low bit)	hex	1854
TPDO4 map2 index	TPDO4 map2 index	hex	1855
TPDO4 map3 sub index and size	TPDO4 map3 sub index (high byte) and size in bits (low bit)	hex	1856
TPDO4 map3 index	TPDO4 map3 index	hex	1857
TPDO4 map4 sub index and size	TPDO4 map4 sub index (high byte) and size in bits (low bit)	hex	1858
TPDO4 map4 index	TPDO4 map4 index	hex	1859
TPDO4 size (words)	TPDO4 size in words		1860
TPDO4 transmission type	TPDO4 number of syncs per transmission 0 to 240 (0 to disable, N for every Nth sync)		1861
TPDO4 event time	TPDO4 event time in ms for async tpdos (0 to disable)	ms	1862
TPDO4 sync window	TPDO4 sync window (not used)		1863
CAN quiet after sleep command	time the controller is quiet (no CAN packets) after a sleep command	ms	1864
CAN quiet after sync loss	time the controller is quiet (no CAN packets) after a sync loss	ms	1865
CAN heartbeat period	period for transmitting the hearbeat signal in ms	ms	1866
BMS Node Firmware Rev	BMS Node Firmware Revision		0
BMS Node LIN Checksum Errors	BMS Node LIN Checksum Error Count		1
BMS Node TTL Comm Timeouts	BMS Node TTL Comm Timeouts		2
BMS Node Absolute SOC	BMS Node Absolute State Of Charge	%	3
BMS Node Relative SOC	BMS Node Relative State Of Charge	%	4
BMS Node Battery Temperature	BMS Node Battery Temperature	Celsius	5
BMS Node Battery Current	BMS Node Battery Current	Amps	6
BMS Node Battery Voltage	BMS Node Battery Voltage	Volts	7
Cell 1 Voltage	BMS Node Battery Cell 1 Voltage	Volts	8
Cell 2 Voltage	BMS Node Battery Cell 2 Voltage	Volts	9
Cell 3 Voltage	BMS Node Battery Cell 3 Voltage	Volts	10
Cell 4 Voltage	BMS Node Battery Cell 4 Voltage	Volts	11
Cell 5 Voltage	BMS Node Battery Cell 5 Voltage	Volts	12
Cell 6 Voltage	BMS Node Battery Cell 6 Voltage	Volts	13
Cell 7 Voltage	BMS Node Battery Cell 7 Voltage	Volts	14
Cell 8 Voltage	BMS Node Battery Cell 8 Voltage	Volts	15
Cell 9 Voltage	BMS Node Battery Cell 9 Voltage	Volts	16
Cell 10 Voltage	BMS Battery Cell 10 Voltage	Volts	17
BMS Current Charge Time	BMS Current Charge Time	Hours	18
BMS Full Charge Capacity	BMS Full Charge Capacity	AmpHours	19
BMS Remaining Charge Capacity	BMS Remaining Charge Capacity	AmpHours	20
BMS Number of Charge Cycles	BMS Battery Number of Charge/Discharge Cycles		21
BMS Maximum Charge Interval	BMS Maximum Charge Interval	Hours	22
POD Firmware Rev	POD Firmware Revision		0
POD LIN Checksum Errors Low	POD LIN Checksum Error Count: Low Word of 32bit value		1
POD LIN Checksum Errors High	POD LIN Checksum Error Count: High Word of 32bit value		2
POD EEPROM Write Counter	Number of times virtual EEPROM has been written.		3
Trip Odometer Low	Trip Odometer: Low word of 32bit value	Km	4
Trip Odometer High	Trip Odometer: High word of 32bit value	Km	5
Total Odometer Low	Total Odometer: Low word of 32bit value		6
Total Odometer High	Total Odometer: High word of 32bit value	Km	7
Wheel Diameter	Wheel Diameter	inches	8
POD Assist Level	POD Assist Level		9
Average Speed	Average speed	Km/h	10
Maximum Vehicle Speed Limit	Battery Range of the battery when 100% Charged	Km/h	11
Lights Command	0 = Headlight/Backlight ON, 1 = Headlight/Backlight ON		12
Display Revision Screen	0 = Main Screen, 2 = Revision Screen		13
Trip Odometer Display Select	0 = Total Odometer, 2 = Trip Odometer		14
Auto Shut Off Timer	Auto Shut Off Timer Count Value in Seconds (Shut off occurs when count > 600 seconds)	seconds	15
Display Firmware Rev	Display Firmware Revision		0
Display LIN Checksum Errors Low	Display LIN Checksum Error Count: Low Word of 32bit value		1
Display LIN Checksum Errors High	Display LIN Checksum Error Count: High Word of 32bit value		2